## Slide 1
Automation with Ansible and Python use Case and examples
Hersh Patel
AT&T Consulting
Oct 29, 2018
© 2017 AT&T Intellectual Property. All rights reserved. AT&T and the Globe logo are registered trademarks of AT&T Intellectual Property. All other marks are the property of their respective owners.

## Slide 2: Goals

## Slide 3
Goals
To give an illustration, example and demonstration of how Ansible Playbook can be used in actual use cases
To give an illustration, example and demonstration of how python and its libraries can be integrated with Ansible or vice versa
Encourage sharing and collaboration
Assumptions
  Heard of Ansible
  Have worked on some scripting before
  Basic understanding of python, but deeper understand will help.

## Slide 4: Enviroment

## Slide 5
Enviroment
Network Overview
  Customer has around 100 sites
  Move from Physical Router(cisco -> juniper) and Firewall(Palo) to VNF
  Move these sites to Flexware
  Move from Customer managed to AT&T Managed
  Site classification unknown
  Number of Subnets = ~ 20 per site

## Slide 6
Traditional (Discovery/Detailed collection)
Traditional Approach to Collection (on network/firewall device)
  Run respective command to collect each required parameter. Example:
    “show ip int brief” -> Grab the state
    “show run” -> Grab ACLs and policy maps
    “show interface” -> Grab Other info
    “show ip bgp neigh” -> check number of BGP neighbors
    “show ip route” -> check routing table
    “show ip bgp” -> check backup routes
    “show run” -> check other misc info
    ….
  Analyze the configuration
  Make necessary changes
  Populate these into an excel document
  Create config from Templates
  Push out Configuration

## Slide 7: High Level

## Slide 8
GIT
Ansible
Ansible modules
Playbooks
Playbooks
Playbooks
Playbooks
Playbooks
Python
Additional Libraries
Access
pandas
Jinja2
csv
OptParse
xlrd/xlwt
sqlite3
Textfsm
ipaddress
pysnmp
paramiko
modules
netmiko
…
json
xml
High Level Tools/Libraries usage
Curl/request

## Slide 9
High Level Steps
Discovery
Log into the device(Ansible)
Execute a command and capture output(Ansible)
Extract applicable data from the output(Ansible)
Processing Info
Analyze Data(Python)
Process the data(Python)
Generating templates(Python)
Configure
Push out Configuration(Ansible)
Validate(Ansible)

## Slide 10
Using Ansible and Python
Use Ansible to fetch the output and Use python to parse/analyze and export
  Run respective command to collect each required parameter. Example:
    “show ip int brief” -> Grab the state
    “show run” -> Grab ACLs and policy maps
    “show interface” -> Grab Other info
    “show ip bgp neigh” -> check number of BGP neighbors
    “show ip route” -> check routing table
    “show ip bgp” -> check backup routes
    “show run” -> check other misc info
  Analyze the configuration
  Make necessary changes
  Populate these into an excel document
  Create config from Templates
  Push out Configuration
  Validate Push

## Slide 11: Examples

## Slide 12
Example Playbook: Device info
Playbook Goal: Document the Following info for all routers on network: “VERSION, ROMMON, HOSTNAME, UPTIME, RUNNING_IMAGE, HARDWARE, SERIAL, CONFIG_REGISTER”.
create_device_info_db.yaml
show_ver
Ansible Playbook
Roles
Tasks
join_across.yaml
IOS: Fetch Output
Copy_to_file
Parse and Output
Scripts
Parse.py
Output
<device>.csv
Order of Execution
<device>.csv
<device>.csv
all_devices.db
aggregated
Playbook
Python

## Slide 13
<device>_LAN_par.csv
Example Playbook: LAN Parameters
Goal: Document all LAN configuration required to migrate from existing Routers and Firewalls
capture_lan.yaml
capture_lan
Roles
Tasks
Fetch Intf paramaters
Copy_to_file
Parse and Output
Scripts
Parse.py
Output
<device>_intf_par.csv
Order of Execution
Playbook
Python
Fetch Intf status
Copy_to_file
Parse and Output
Join Data
join_intf_tables.py
<device>_state_par.csv
Combine
Ansible Playbook
Continued

## Slide 14
interface_process.py
<device>_LAN_par.csv
Example Playbook: LAN Parameters
Goal: Document all LAN configuration required to migrate from existing Routers
capture_lan.yaml
capture_lan
Roles
Tasks
Scripts
Output
Order of Execution
Playbook
Python
Join Data
join_intf_tables.py
Ansible Playbook
Process and Output
<device>_RTR_LAN.csv
<device>_ANIRA_LAN.csv
Use as inputs
FW.cvs
fw.py

## Slide 15
Example Script: Palo LAN
Goal: Document all LAN configuration required to migrate from existing Firewalls.
  Note: ran into issues with Anisible and Palo “406”, used postman/Curl/request
Scripts
Output
Order of Execution
Python
<firewall>.cvs
palo_parse_lan.py
fetch_cfg.py
<firewall>.xml
Use as inputs

## Slide 16
Example: Templating
Goal: Automate template generation for devices based on excel database
Scripts
Output
Order of Execution
Python
<anira>.cfg
gen_cfg.py
<rtr>.cfg
site_db.xlsx
Combination of info collected from scripts and by hand
Jinja2
Router_hierarchical_templates
ANIRA_hierarchical_templates
Use as inputs
Use as inputs for variable, conditional and loops
Router_hierarchical_templates
ANIRA_hierarchical_templates

## Slide 17: Summary

## Slide 18
Summary
Ansible
  Excellent at fetching and Configuring devices
  Framework provides consistency and predictability
  Limited functionality within itself
Python and other libraries
  Great for extending capabilities of Ansible
  Takes time to develop
Lots of other tools and frameworks……
Getting Started
  Be active in looking for use cases, this is the best way to learn
  Build up your library and don’t forget to document
  Don’t re-invent a wheel, there are lot of libraries out there
  Will not happen over night
I am happy to share, importantly happy to collaborate.